## Slide 1: Défis dans l’optimisation du placement et du chainage des microservices hétérogènes
DOYEN Guillaume – IMT Atlantique
MAGNOUCHE Hichem - UTT
PRODHON Caroline - UTT
30/04/2021
Session : « Optimisation dans les réseaux de télécommunication intelligents »

## Slide 2: Sommaire
Développement des services internet à faible latence
Orchestration de fonction de réseau virtuelle (VNF)
Approche microservice appliquée à l’orchestration de VNF
Bilan et perspectives

## Slide 3: Sommaire
Développement des services internet à faible latence
Orchestration de fonction de réseau virtuelle (VNF)
Approche microservice appliquée à l’orchestration de VNF
Bilan et perspectives

## Slide 4: Projet MOSAICO
Développement de services à faible latence
  Temps de transit limité au sein du réseau
  Exemples
    Pilotage de drones
    Télé-chirurgie
    Cloud Gaming
Objectifs du projet
  Utilisation de microservices
  Utilisation de composants technologiques hétérogènes
  Développement d’une approche d’orchestration de microservices

## Slide 5: Virtualisation de fonctions de réseau
NFV (Network Function Virtualisation) initiée et standardisée par l’ETSI* en 2013
  Principe de séparation des fonctions de réseau du matériel physique
  Virtualisation des fonctions de réseau : VNF (Virtualized Network Function)
  Exécution des fonctions sur des serveurs génériques
  Orchestration centralisée des fonctions exécutées
Avantages
  Agilité dans l’installation ou dans la suppression de fonction de réseau
  Réduction des coûts de maintenance et de mise à niveau du réseau
  Réduction de la consommation électrique du réseau
  Réduction de l’espace nécessaire aux équipements matériels
Exemples de VNF
  Firewall, IDS (Intrusion Detection System), Video Optimizer

## Slide 6: Exemple d’une infrastructure réseau NFV

## Slide 7: Sommaire
Développement des services internet à faible latence
Orchestration de fonction de réseau virtuelle (VNF)
Approche microservice appliquée à l’orchestration de VNF
Bilan et perspectives

## Slide 8: L’orchestration dans le contexte réseau
L’orchestration de fonction de réseau permet
  le contrôle des ressources réseau
  leur déploiement
  leur gestion
  leur optimisation
But : répondre aux demandes de service réseau
  Contraintes techniques : latence de bout en bout, débit, consommation d’énergie
L’orchestration se fait à travers différents décisions
  Décision de placement (VNF-P)
  Décision de chainage (VNF-C)
  Décision d’ordonnancement (VNF-S)

## Slide 9
Décisions d’orchestration : exemple

## Slide 10: Etat de l’art : classification des décisions d’orchestration
Décisions d’orchestration
VNF-P
Uncapacitated VNF-C
Capacitated VNF-PC
Uncapacitated VNF-PC
Avec contrainte de précédence
VNF-S
VNF-C
VNF-PS
Sans contrainte de précédence
Capacitated VNF-C
Dynamic VNF-C
Static VNF-C
VNF-P
VNF-R
VNF-PR
1-VNF-PR
n-VNF-PR
Uncapacitated VNF-PR
Capacitated VNF-PR
[13][26][8]
[11][17][23][30]
[15][16][25][28]
[19][22]
[29]
[31][14][24][18][6]
[2][7]
[27]
[1][20]
[4][3][5][12][32]
[9][10][21]

## Slide 11: Sommaire
Développement des services internet à faible latence
Orchestration de fonction de réseau virtuelle (VNF)
Approche microservice appliquée à l’orchestration de VNF
Bilan et perspectives

## Slide 12: Architecture monolithique/microservice
Microservice : technique de développement structurant une application en composants basiques (µService)
  Faible couplage entre les µServices
  Fonctionnement asynchrone des µServices
Utilisation de l’approche microservice dans le Cloud
Inconvénients des architectures monolithiques
  Chevauchement des fonctionnalités au sein d’une même SFC
  Gaspillage de cycle CPU
    25% de cycles CPU dans du traitement redondant [33]
  Inflexibilité dans la mise à l’échelle
C1
C3
C1
C4
C1
C2
NF1
NF2
NF3

## Slide 13: Architecture monolithique/microservice
Avantages du passage au microservice
Approche microservices
Approche monolithique
Exemple [34]:
Nécessité de repenser les décisions d’orchestration
  Densification de la communication
  Fonctionnement asynchrone des microservices
  Parallélisme ainsi que la gestion des cycles de vie des paquets
  Agrégation des fonctionnalités
  Flexibilité
  Développements, M.A.J et tests simplifiés
  Optimisation des ressources
  Meilleure tolérance aux pannes

## Slide 14: Microservice : revue de littérature dans le contexte Cloud
N.Jahromi et al [35] proposent une architecture microservice pour les composants CDN
  CDN décomposés en µServices
  S’inspirent des concepts NFV pour l’orchestration
  Décisions d’orchestration non traitées
Y.Yinbo et al [36] traitent la problématique de placement et de chainage de microservices
  Approche permettant : l’instanciation, le placement ainsi que le chainage
  Algorithme de placement de type Glouton
  Performance lésée comparée aux méthodes monolithiques

## Slide 15: Microservice : revue de littérature dans le contexte d’orchestration de VNF
H.Hawilo et al. [37] présentent les principaux défis et exigences
Proposent un modèle MILP pour le VNF-P
  Contraintes
    Rejeter les serveurs violant les délais limites de communication entre les µServices
    Sélectionner les serveurs respectant les contraintes d’affinité/anti-affinité
    Contraintes d’ancrage des µServices et contraintes de zone orbitale
      Zone de placement respectant la limite de délais de latence
  Objectif
    Minimiser les délais de latence
  Environnement de technologie homogène

## Slide 16: Microservice : revue de littérature dans le contexte d’orchestration de VNF
M.Zili et al. [38] développent le Framework MicroNF
  Traitent les problématiques de placement, chainage ainsi que d’ordonnancement
  Approche développée sur trois axes
    Reconstruction des SFCs
      Réutilisation des µServices
    Algorithme de placement permettant la consolidation de différents µServices dans les VMs
    Nouvelle approche de mise à l’échelle
      Evitant la duplication de service
      Minimisant la communication
  Objectif
    Minimiser les coûts de communication

## Slide 17: Sommaire
Développement des services internet à faible latence
Orchestration de fonction de réseau virtuelle (VNF)
Approche microservice appliquée à l’orchestration de VNF
Bilan et perspectives

## Slide 18: Bilan et perspectives
Limites de l’état de l’art dans le contexte de la minimisation de la latence de bout-en-bout
  Amélioration de la performance des algorithmes d’orchestration
  L’utilisation de contraintes réalistes
  L’utilisation de technologies hétérogènes
  Cohabitation de l’approche monolithique et microservice
Perspectives
  À court terme
    Traiter la problématique Capacitated VNF-PC
      Architecture Microservice
      Dans un objectif de minimisation de la latence de bout en bout
      Dans un environnement de technologies hétérogènes
  À moyen terme
    Inclure l’aspect dynamique dans la gestion des demandes de service
    Inclure l’aspect de cohabitation entre l’approche microservice et monolithique

## Slide 19: Questions
Q & A

## Slide 20: Références
  [1] : B. Addis et al. “Virtual network functions placement and routing optimization”. In: 2015 IEEE 4th International Conference on Cloud Networking (CloudNet). 2015, pp. 171–177. doi: 10.1109/ CloudNet.2015.7335301
  [2] : Bernardetta Addis, Giuliana Carello, and Meihui Gao. “On a virtual network functions placement and routing problem: Some properties and a comparison of two formulations”. In: Networks 75 (Nov. 2019). doi: 10.1002/net.21915
  [3] : O. Alhussein et al. “Joint VNF Placement and Multicast Traffic Routing in 5G Core Networks”. In: 2018 IEEE Global Communications Conference (GLOBECOM). 2018, pp. 1–6. doi: 10.1109/ GLOCOM.2018.8648029
  [4] : Zaid Allybokus et al. “Virtual Function Placement for Service Chaining with Partial Orders and Anti-Affinity Rules”. In: Networks 71 (May 2017). doi: 10.1002/net.21768
  [5] : M. F. Bari et al. “On orchestrating virtual network functions”. In: 2015 11th International Conference on Network and Service Management (CNSM). 2015, pp. 50–56. doi: 10.1109/CNSM.2015. 7367338
  [6] : Chao Bu et al. “Enabling Adaptive Routing Service Customization via the Integration of SDN and NFV”. In: Journal of Network and Computer Applications 93 (June 2017). doi: 10.1016/j. jnca.2017.05.010
  [7] : Martín Casado et al. “Virtualizing the network forwarding plane”. In: (Jan. 2010), p. 8. doi: 10.1145/1921151.1921162
  [8] : R. Cohen et al. “Near optimal placement of virtual network functions”. In: 2015 IEEE Conference on Computer Communications (INFOCOM). 2015, pp. 1346–1354. doi: 10.1109/INFOCOM.2015. 7218511
  [9] : R. Gouareb, V. Friderikos, and A. H. Aghvami. “Delay Sensitive Virtual Network Function Placement and Routing”. In: 2018 25th International Conference on Telecommunications (ICT). 2018, pp. 394–398. doi: 10.1109/ICT.2018.8464883
  [10] : Abhishek Gupta et al. “On service-chaining strategies using Virtual Network Functions in operator networks”. In: Computer Networks 133 (2018), pp. 1–16. issn: 1389-1286. doi: https://doi.org/ 10.1016/j.comnet.2018.01.028. url: http://www.sciencedirect.com/science/article/ pii/S1389128618300379
  [11] : H. Huang et al. “Service Chaining for Hybrid Network Function”. In: IEEE Transactions on Cloud Computing 7.4 (2019), pp. 1082–1094. doi: 10.1109/TCC.2017.2721401

## Slide 21: Références
  [12] : N. Kiji et al. “Virtual Network Function Placement and Routing Model for Multicast Service Chaining Based on Merging Multiple Service Paths”. In: 2019 IEEE 20th International Conference on High Performance Switching and Routing (HPSR). 2019, pp. 1–6. doi: 10.1109/HPSR.2019. 8807998
  [13] : G. Larysa, S. Mariia, and S. Svitlana. “Method for resource allocation of virtualized network functions in hybrid environment”. In: 2016 IEEE International Black Sea Conference on Communications and Networking (BlackSeaCom). 2016, pp. 1–5. doi: 10.1109/BlackSeaCom.2016.7901546
  [14] : Giwon Lee et al. “Optimal Flow Distribution in Service Function Chaining”. In: The 10th International Conference on Future Internet. CFI ’15. Seoul, Republic of Korea: Association for Computing Machinery, 2015, pp. 17–20. isbn: 9781450335645. doi: 10.1145/2775088.2775103. url: https://doi.org/10.1145/2775088.2775103
  [15] : J. Li et al. “Delay-Aware VNF Scheduling: A Reinforcement Learning Approach With Variable Action Set”. In: IEEE Transactions on Cognitive Communications and Networking 7.1 (2021), pp. 304–318. doi: 10.1109/TCCN.2020.2988908
  [16] : J. Li et al. “Reinforcement Learning Based VNF Scheduling with End-to-End Delay Guarantee”. In: 2019 IEEE/CIC International Conference on Communications in China (ICCC). 2019, pp. 572– 577. doi: 10.1109/ICCChina.2019.8855889
  [17] : Z. Li and Y. Yang. “Placement of Virtual Network Functions in Hybrid Data Center Networks”. In: 2017 IEEE 25th Annual Symposium on High-Performance Interconnects (HOTI). 2017, pp. 73–79. doi: 10.1109/HOTI.2017.15
  [18] : J. Liu et al. “On Dynamic Service Function Chain Deployment and Readjustment”. In: IEEE Transactions on Network and Service Management 14.3 (2017), pp. 543–553. doi: 10.1109/TNSM. 2017.2711610
  [19] : F. Lucrezia et al. “Introducing network-aware scheduling capabilities in OpenStack”. In: Proceedings of the 2015 1st IEEE Conference on Network Softwarization (NetSoft). 2015, pp. 1–5. doi: 10.1109/NETSOFT.2015.7116155
  [20] : M. C. Luizelli et al. “Piecing together the NFV provisioning puzzle: Efficient placement and chaining of virtual network functions”. In: 2015 IFIP/IEEE International Symposium on Integrated Network Management (IM). 2015, pp. 98–106. doi: 10.1109/INM.2015.7140281
  [21] : Marcelo Caggiani Luizelli et al. “A fix-and-optimize approach for efficient and large scale virtual network function placement and chaining”. In: Computer Communications 102 (2017), pp. 67– 77. issn: 0140-3664. doi: https://doi.org/10.1016/j.comcom.2016.11.002.

## Slide 22: Références
  [22] : R. Mijumbi et al. “Design and evaluation of algorithms for mapping and scheduling of virtual network functions”. In: Proceedings of the 2015 1st IEEE Conference on Network Softwarization (NetSoft). 2015, pp. 1–9. doi: 10.1109/NETSOFT.2015.7116120
  [23] : H. Moens and F. D. Turck. “VNF-P: A model for efficient placement of virtualized network functions”. In: 10th International Conference on Network and Service Management (CNSM) and Workshop. 2014, pp. 418–423. doi: 10.1109/CNSM.2014.7014205
  [24] : Y. Nam, S. Song, and J. Chung. “Clustered NFV Service Chaining Optimization in Mobile Edge Clouds”. In: IEEE Communications Letters 21.2 (2017), pp. 350–353. doi: 10.1109/LCOMM.2016. 2618788
  [25] : C. Pham, N. H. Tran, and C. S. Hong. “Virtual Network Function Scheduling: A Matching Game Approach”. In: IEEE Communications Letters 22.1 (2018), pp. 69–72. doi: 10.1109/LCOMM.2017. 2747509
  [26] : W. Rankothge et al. “Optimizing Resource Allocation for Virtualized Network Functions in a Cloud Center Using Genetic Algorithms”. In: IEEE Transactions on Network and Service Management 14.2 (2017), pp. 343–356. doi: 10.1109/TNSM.2017.2686979
  [27] : ] J. F. Riera et al. “TeNOR: Steps towards an orchestration platform for multi-PoP NFV deployment”. In: 2016 IEEE NetSoft Conference and Workshops (NetSoft). 2016, pp. 243–250. doi: 10.1109/NETSOFT.2016.7502419
  [28] : J. F. Riera et al. “Virtual network function scheduling: Concept and challenges”. In: 2014 International Conference on Smart Communications in Network Technologies (SaCoNeT). 2014, pp. 1–5. doi: 10.1109/SaCoNeT.2014.6867768
  [29] : Sahel Sahhaf et al. “Network service chaining with optimized network function embedding supporting service decompositions”. In: Computer Networks 93 (Oct. 2015). doi: 10.1016/j.comnet. 2015.09.035
  [30] : Andrea Tomassilli. “Towards next generation networks with SDN and NFV”. PhD thesis. June 2019
  [31] : Peng Wang et al. “Dynamic function composition for network service chain: Model and optimization”. In: Computer Networks 92 (2015). Software Defined Networks and Virtualization, pp. 408– 418. issn: 1389-1286. doi: https://doi.org/10.1016/j.comnet.2015.07.020. url: https: //www.sciencedirect.com/science/article/pii/S1389128615003266
  [32] : S. Q. Zhang et al. “Joint NFV placement and routing for multicast service on SDN”. In: NOMS 2016 - 2016 IEEE/IFIP Network Operations and Management Symposium. 2016, pp. 333–341. doi: 10.1109/NOMS.2016.7502829

## Slide 23: Références
  [33] : Sekar, Vyas & Egi, Norbert & Ratnasamy, Sylvia & Reiter, Michael & Shi, Guangyu. (2012). Design and implementation of a consolidated middlebox architecture. 24-24.
  [34] : S. R. Chowdhury, M. A. Salahuddin, N. Limam and R. Boutaba, "Re-Architecting NFV Ecosystem with Microservices: State of the Art and Research Challenges," in IEEE Network
  [35]: N. T. Jahromi, R. H. Glitho, A. Larabi and R. Brunner, "An NFV and microservice based architecture for on-the-fly component provisioning in content delivery networks," 2018 15th IEEE Annual Consumer Communications & Networking Conference (CCNC), 2018, pp. 1-7, doi: 10.1109/CCNC.2018.8319227
  [36] Yinbo, Yu & Yang, Jianfeng & Guo, Chengcheng & Zheng, Hong & He, Jiancheng. (2019). Joint optimization of service request routing and instance placement in the microservice system. Journal of Network and Computer Applications. 147. 102441. 10.1016/j.jnca.2019.102441.
  [37] : Hassan Hawilo, M. Jammal and A. Shami, "Exploring Microservices as the Architecture of Choice for Network Function Virtualization Platforms," in IEEE Network, vol. 33, no. 2, pp. 202-210, March/April 2019, doi: 10.1109/MNET.2019.1800023.
  [38] : Z. Meng, J. Bi, H. Wang, C. Sun and H. Hu, "MicroNF: An Efficient Framework for Enabling Modularized Service Chains in NFV" in IEEE Journal on Selected Areas in Communications, vol. 37, no. 8, pp. 1851-1865, Aug. 2019, doi: 10.1109/JSAC.2019.2927069